## Slide 1
ROOMAN TECHNOLOGIES
Cybersecurity Internship Program
Phase 2 — Build
Establish an IPSec VPN Tunnel
Between Head Office & Datacenter
Name
Nithin Nayaka V N
Tool
Cisco Packet Tracer 9.0
Domain
Cybersecurity
Phase
02 — Build

## Slide 2
Phase 2 Roadmap — 5-Day Build Plan
Day 1
Topology
Place 15 devices
Connect cables
Day 2
IP Config
Assign IPs to all
routers & PCs
Day 3
Routing
Static routes for
end-to-end reach
Day 4
IPSec VPN
IKE + Transform
+ Crypto Map
Day 5
Testing
Ping + verify
crypto SA
✔ Deliverable: IPSec VPN tunnel QM_IDLE ACTIVE with 0% packet loss across 15 devices
Rooman Technologies | Cybersecurity Internship | Phase 2 — Build

## Slide 3
Day 1 — Network Topology (15 Devices)
Rooman Technologies | Cybersecurity Internship | Phase 2 — Build | Day 1: Topology Design

## Slide 4
Day 2 — IP Address Configuration
Device | Interface | IP Address | Role
HO-Router | Gi0/0 | 192.168.1.1 /24 | HO LAN Gateway
HO-Router | Gi0/1 | 10.0.0.1 /30 | WAN to ISP
ISP-Router | Gi0/0 | 10.0.0.2 /30 | WAN facing HO
ISP-Router | Gi0/1 | 10.0.0.5 /30 | WAN facing DC
DC-Router | Gi0/0 | 10.0.0.6 /30 | WAN to ISP
DC-Router | Gi0/1 | 192.168.2.1 /24 | DC LAN Gateway
PC0–PC4 (HO) | Fa0 | 192.168.1.x /24 | GW: 192.168.1.1
PC5–PC9 (DC) | Fa0 | 192.168.2.x /24 | GW: 192.168.2.1
Rooman Technologies | Cybersecurity Internship | Phase 2 — Build | Day 2: IP Configuration

## Slide 5
Day 3 — Static Routing Configuration
HO-Router
ip route 192.168.2.0 255.255.255.0 10.0.0.2
ip route 10.0.0.4 255.255.255.252 10.0.0.2
✓ Routes applied & saved
ISP-Router
ip route 192.168.1.0 255.255.255.0 10.0.0.1
ip route 192.168.2.0 255.255.255.0 10.0.0.6
✓ Routes applied & saved
DC-Router
ip route 192.168.1.0 255.255.255.0 10.0.0.5
ip route 10.0.0.0 255.255.255.252 10.0.0.5
✓ Routes applied & saved
Baseline Test (before VPN): PC0 → ping 192.168.2.2 — SUCCESS ✓ (unencrypted baseline confirmed)
Rooman Technologies | Cybersecurity Internship | Phase 2 — Build | Day 3: Static Routing

## Slide 6
Day 4 — IPSec VPN: IKE Phase 1 (ISAKMP Policy)
Encryption
AES-128
Hash
SHA-1
Auth
Pre-Shared Key
DH Group
Group 2 (1024-bit)
Lifetime
86400 sec (24 hrs)
HO-Router & DC-Router:
crypto isakmp policy 10
encryption aes 128
hash sha
authentication pre-share
group 2
lifetime 86400
exit
! HO-Router PSK:
crypto isakmp key ROOMAN@VPN
address 10.0.0.6
! DC-Router PSK:
crypto isakmp key ROOMAN@VPN
address 10.0.0.1
Rooman Technologies | Cybersecurity Internship | Phase 2 — Build | Day 4: IPSec Configuration

## Slide 7
Day 4 — IKE Phase 2, ACL & Crypto Map
Transform Set
crypto ipsec transform-set
TSET esp-aes
esp-sha-hmac
ESP-AES: Encrypts data
ESP-SHA-HMAC: Integrity
Mode: Tunnel
ACL (Interesting Traffic)
! HO-Router:
access-list 101 permit ip
192.168.1.0 0.0.0.255
192.168.2.0 0.0.0.255
! DC-Router:
access-list 101 permit ip
192.168.2.0 0.0.0.255
192.168.1.0 0.0.0.255
Crypto Map (VPNMAP)
crypto map VPNMAP 10
ipsec-isakmp
set peer 10.0.0.6
set transform-set TSET
match address 101
int Gi0/1
crypto map VPNMAP
Applied to WAN interfaces: HO-Router → Gi0/1 | DC-Router → Gi0/0
Rooman Technologies | Cybersecurity Internship | Phase 2 — Build | Day 4: IPSec Configuration

## Slide 8
Day 5 — Testing & Verification
show crypto isakmp sa → QM_IDLE ACTIVE ✓
PC0 → ping 192.168.2.2 → 0% loss ✓
26
pkts encrypt
23
pkts decrypt
QM_IDLE
Tunnel State
0%
Packet Loss
Rooman Technologies | Cybersecurity Internship | Phase 2 — Build | Day 5: Testing & Verification

## Slide 9
Day 5 — show crypto ipsec sa Output
Rooman Technologies | Cybersecurity Internship | Phase 2 — Build | Verification: IPSec SA Details

## Slide 10
Simulation Mode — Packet Flow Visualization
IPSec packets (red) visible between routers — confirms traffic is encrypted through the tunnel
Rooman Technologies | Cybersecurity Internship | Phase 2 — Build | Simulation Verification

## Slide 11
Phase 2 Summary — All Deliverables Met
✓
15-device topology built in Packet Tracer
✓
IP addresses configured on all 3 routers & 10 PCs
✓
Static routing verified (end-to-end pre-VPN ping)
✓
Security license activated (securityk9 package)
✓
IKE Phase 1 policy: AES-128, SHA-1, PSK, Group 2
✓
IKE Phase 2: Transform set TSET (ESP-AES + SHA-HMAC)
✓
Crypto map VPNMAP applied to WAN interfaces
✓
Tunnel status: QM_IDLE ACTIVE (conn-id 1090)
✓
Encrypted packets: 26 encaps / 23 decaps confirmed
✓
PC0 → PC9 ping: 4/4 packets, 0% loss
🎉 Phase 2 Complete — IPSec VPN Tunnel Successfully Established!